| Vertical System |
| --- |
| Analog (ProBus Input) Bandwidth @ 50 Ω (-3 dB) | 600 MHz (model 66Zi) 400MHz (model 64Zi) (≥2 mV/div) |
| Analog (ProBus Input) Bandwidth @ 1 MΩ (-3 dB) | 500 MHz (typical) (model 66Zi) 400MHz (model 64Zi) |
| Rise Time (typical, 10-90%, 50 Ω) | 625 ps (typical) model 66Zi) 875 ps (model 64Zi) |
| Rise Time (typical, 20-80%, 50 Ω) | 435 ps (typical) model 66Zi) 650 ps (model 64Zi) |
| Input Channels | 4 |
| Bandwidth Limiters | 20MHz, 100 MHz, 200MHz, (350 MHz only 66Zi) |
| Input Impedance | 50 Ω+/-2% or 1 MΩ¦¦17pF, 10 MΩ ¦¦ 17 pF with supplied Probe |
| Input Coupling | 1 MΩ: AC, DC, GND; 50 Ω: DC, GND |
| Maximum Input Voltage | 50 Ω: 5V RMS ± 10V peak 1 MΩ: 400 V max. (DC + peak AC < 10 kHz) |
| Channel-Channel Isolation | > 300:1 up to rated BW |
| Vertical Resolution | 12 bits; up to 15 bits with enhanced resolution (ERES) |
| Sensitivity | 50 Ω: 1 mV-1 V/div, fully variable; 1 MΩ: 1 mV-10 V/div, fully variable |
| DC Vertical Gain Accuracy (Gain Component of DC Accuracy) | ±0.5% F.S., offset at 0V |
| Offset Range | 50 Ω: ±1.6 V @ 1 mV - 4.95 mV ±4 V @ 5mV - 9.9 mV ±8 V @ 10mV - 19.8 mV ±10 V @ 20mV - 1V 1 MΩ: ±1.6 V @ 1 mV - 4.95 mV ±4 V @ 5mV - 9.9 mV ±8 V @ 10mV - 19.8 mV ±16 V @ 20mV - 100 mV ±80 V @ 102mV - 198 mV ±160 V @ 200mV - 1V ±400V @ 1.02 V-10 V/div |
| DC Vertical Offset Accuracy | ±(1% of offset setting +0.2% of full scale + 0.02% max offset + 1 mV) |
| Horizontal System |
| Timebases | Internal timebase common to 4 input channels; an external clock may be applied at the auxiliary input |
| Time/Division Range | Real-Time: 20 ps/div-1600 s/div; RIS mode: 20 ps/div - 10 ns/div; Roll mode: up to 1600 s/div (roll mode is user selectable at ≥100 ms/div and ≤5 MS/s) |
| Clock Accuracy | ≤ 1.5 ppm +(aging of 0.5 ppm/yr from last calibration) |
| Time Interval Accuracy | < 0.06 / SR + (clock accuracy* Reading) (rms) |
| Trigger and Interpolator Jitter | ≤ 5.5 psrms (typical) <0.1 ps RMS (typical, software assisted) |
| Sample Rate and Delay Time Accuracy | Equal to Clock Accuracy |
| Channel-Channel Deskew Range | ±9 x time/div. setting, 100 ms max., each channel |
| External Timebase Reference (Input) | 10MHz +/-25ppm via Lbus BNC adaptor |
| External Timebase Reference (Output) | 10MHz, 3.5 dBm +/-1dBm, syncronized to reference being used by user (internal or external reference) via Lbus BNC adaptor |
| External Clock | DC to 100 MHz; (50 Ω/1 MΩ), EXT BNC input, Minimum rise time and amplitude requirements apply at low frequencies. |
| Acquisition System |
| Single-Shot Sample Rate/Ch | 2 GS/s on 4 Ch |
| Random Interleaved Sampling (RIS) | 100 GS/s, user selectable for repetitive signals (20 ps/div to 10 ns/div) |
| Maximum Trigger Rate | 1,000,000 waveforms/second (in Sequence Mode, up to 4 channels) |
| Intersegment Time | 2 us |
| Memory Options (4 Ch / 2 Ch / 1Ch) | L-128 Option: 128M / 128M / 128M (60,000) XL - 256 Option: 256M / 256M / 256M (125,000) |
| Standard Memory (4 Ch / 2 Ch / 1Ch) (Number of Segments) | 64M/64M/64M (30,000) |
| Acquisition Processing |
| Averaging | Summed averaging to 1 million sweeps; continuous averaging to 1 million sweeps |
| Enhanced Resolution (ERES) | From 12.5 to 15 bits vertical resolution |
| Envelope (Extrema) | Envelope, floor, or roof for up to 1 million sweeps |
| Interpolation | Linear or Sin x/x |
| Triggering System |
| Modes | Normal, Auto, Single, and Stop |
| Sources | Any input channel, Ext, Ext/10, or line; slope and level unique to each source (except line trigger) |
| Coupling Mode | DC, AC, HFRej, LFRej |
| Pre-trigger Delay | 0-100% of memory size (adjustable in 1% increments of 100 ns) |
| Post-trigger Delay | 0-50,000,000,000 divisions in real time mode, limited at slower time/div settings or in roll mode |
| Hold-off by Time | From 2 ns up to 20 s or from 1 to 99,999,999 events |
| Internal Trigger Range | ±4.1 div from center (typical) |
| Trigger Sensitivity with Edge Trigger (Ch 1–4) ProBus Inputs | 2 div @ < 600 MHz 1.5 div @< 300 MHz 1 div @ < 200 MHz 0.9 div @<10 MHz (DC, AC, and LFRej coupling, ≥ 10 mV/div, 50 Ω) |
| External Trigger Sensitivity, (Edge Trigger) | 2 div @ < full Bandwidth 1.5 div @ < 300 MHz 1 div @ <200 MHz 0.9 div @<10 MHz (DC, AC, and LFRej coupling) |
| External Trigger Input Range | Ext (±0.4 V); Ext/10 (±4 V) |
| Max. Trigger Frequency, SMART Trigger | 600 MHz @ ≥ 10 mV/div (minimum triggerable width 1.2 ns) |
| Basic Triggers |
| Edge | Triggers when signal meets slope (positive, negative, or either) and level condition. |
| Window | Triggers when signal exits a window defined by adjustable thresholds |
| TV-Composite Video | Triggers NTSC or PAL with selectable line and field; HDTV (720p, 1080i, 1080p) with selectable frame rate (50 or 60 Hz) and Line; or CUSTOM with selectable Fields (1-8), Lines (up to 2000), Frame Rates (25, 30, 50, or 60 Hz), Interlacing (1:1, 2:1, 4:1, 8:1), or Synch Pulse Slope (Positive or Negative). |
| SMART Triggers |
| State or Edge Qualified | Triggers on any input source only if a defined state or edge occurred on another input source. Delay between sources is selectable by time or events. |
| Qualified First | In Sequence acquisition mode, triggers repeatably on event B only if a defined pattern, state, or edge (event A) is satisfied in the first segment of the acquisition. Holdoff between sources is selectable by time or events. |
| Dropout | Triggers if signal drops out for longer than selected time between 1 ns and 20 s. |
| Pattern | Logic combination (AND, NAND, OR, NOR) of 5 inputs (4 channels and external trigger input, or 2 channels and external input for 62Xi). Each source can be high, low, or don't care. The High and Low level can be selected independently. Triggers at start or end of the pattern. |
| SMART Triggers with Exclusion Technology |
| Glitch | Triggers on positive or negative glitches with widths selectable as low as 200ps (depending on oscilloscope bandwidth) to 20 s, or on intermittent faults. |
| Width (Signal or Pattern) | Triggers on positive or negative glitches with widths selectable as low as 200ps (depending on oscilloscope bandwidth) to 20 s, or on intermittent faults. |
| Interval (Signal or Pattern) | Triggers on intervals selectable between 1 ns and 20 s. |
| Timeout (State/Edge Qualified) | Triggers on any source if a given state (or transition edge) has occurred on another source. Delay between sources is 1 ns to 20 s, or 1 to 99,999,999 events. |
| Runt | Trigger on positive or negative runts defined by two voltage limits and two time limits. Select between 1 ns and 20 ns. |
| Slew Rate | Trigger on edge rates. Select limits for dV, dt, and slope. Select edge limits between 1 ns and 20 ns. |
| Exclusion Triggering | Trigger on intermittent faults by specifying the expected behavior and triggering when that condition is not met |
| Cascade (Sequence) Triggering |
| Capability | Arm on "A" event, then Trigger on "B" event. Or Arm on "A" event, then Qualify on "B" event, and Trigger on "C" event. Or Arm on "A" event, then Qualify on "B" then "C" event, and Trigger on "D" event |
| Types | A, B, C, or D event: Edge, Glitch, Width, Window, Dropout, Interval, Runt, Slew Rate, Pattern (analog), or Measurement. |
| Holdoff | Holdoff between A and B, B and C, C or D, or any is selectable by time or number of events |
| Reset | Reset between A and B, B and C, C and D, or any combination is selectable in time or number of events |
| Measurement Trigger |
| Measurement Trigger | Trigger on Measurement with qualified limits. Can be used as only trigger or last event in cascade. |
| Low Speed Serial Protocol Triggering (Optional) |
| Optionally available | I2C, SPI (SPI, SSPI, SIOP), UART-RS232, CAN, LIN, FlexRay, MIL-STD-1553, USB 1.x/2.0 |
| Color Waveform Display |
| Type | Color 12.1" widescreen flat panel TFT-Active Matrix with high resolution touch screen |
| Resolution | WXGA; 1280 x 800 pixels. |
| Number of traces | Display a maximum of 8 traces. Simultaneously display channel, zoom, memory and math traces. |
| Grid Styles | Auto, Single, Dual, Quad, Octal, X-Y, Single+X-Y, Dual+X-Y |
| Waveform Representation | Sample dots joined, or sample dots only |
| Internal Waveform Memory |
| Internal Waveform Memory | 4 active waveform memory traces (M1-M4) store 16 bit/point full length waveforms. Waveforms can be stored to any number of files limited only by the data storage media capacity. |
| LeCroy WaveStream™ Fast Viewing Mode |
| Intensity | 256 Intensity Levels, 1-100% adjustable via front panel control |
| Types | Analog only |
| Number of Channels | up to 4 simultaneously |
| Max Sampling Rate | 2 GS/s |
| Waveforms/second (continuous) | up to 20,000 Waveforms/second |
| Operation | Front panel toggle between normal real-time mode and LeCroy WaveStream Fast Viewing mode |
| Automatic Setup |
| Auto Setup | Automatically sets timebase, trigger, and sensitivity to display a wide range of repetitive signals |
| Find Vertical Scale | Automatically sets the vertical sensitivity and offset for the selected channel to display a waveform with the maximum dynamic range |
| Probes |
| Probes | Qty. (4) ÷10 Passive Probes |
| Probing System | Probus. Automatically detects and supports a variety of compatible probes |
| Scale Factors | Automatically or manually selected depending on probe used |
| Calibration Output | Default is 1kHz square wave, 1Vpp (typical), output to probe hook. Settable from 250 Hz to 1 MHz square wave; 50 mV to 1.0V. |
| Analog Persistence Display |
| Analog and Color-Graded Persistence | Variable saturation levels; stores each trace's persistence data in memory |
| Trace Selection | Activate persistence on all or any combination of traces |
| Sweep Display Modes | All accumulated, or all accumulated with last trace highlighted |
| Persistence Types | Select analog, color, or three-dimensional |
| Persistence Aging | Select from 500 ms to infinity |
| High Speed Digitizer Output (Option) |
| Type | Not Available |
| Transfer Rate | Not Available |
| Output Protocol | Not Available |
| Control Protocol | Not Available |
| Command Set | Not Available |
| Processor/CPU |
| Type | Intel E5300 Pentium Dual Core (3.2 GHz) |
| Processor Memory | 4 GB standard |
| Operating System | Microsoft Windows® 7 Pro 64 bit Embedded |
| Real Time Clock | Date and time displayed with waveform in hardcopy files. SNTP support to synchronize to precision internal clocks. |
| Zoom Expansion Traces |
| Zoom Expansion Traces | Display up to 4 Zoom and 8 Math/Zoom traces |
| Setup Storage |
| Front Panel and Instrument Status | Store to the internal hard drive, over the network, or to a USB-connected peripheral device. |
| Interface |
| Remote Control | Via Windows Automation, or via LeCroy Remote Command Set |
| Network Communication Standard | VXI-11 or VICP, LXI Class C (v1.2) Compliant |
| GPIB Port (optional) | Supports IEEE - 488.2 (External) |
| LSIB Port (optional) | Not Available |
| USB (Device) | 1 USBTMC port |
| Ethernet Port | Supports 10/100/1000BaseT Ethernet interface (RJ45 port) |
| USB Ports | minimum 4 total (incl. 2 front panel) USB 2.0 ports support Windows compatible devices |
| External Monitor Port | 15 pin D-Type WXGA compatible DB-15 to support customer-supplied external monitor. Includes support for extended desktop operation with WXGA resolution on second monitor. |
| Serial Port | Not available |
| Peripheral Bus | LeCroy LBUS standard |
| Auxiliary Input |
| Signal Types | Select External Trigger or External Clock Input on the front panel |
| Coupling | 50 Ω: DC; 1 MΩ: AC, DC, GND |
| Max. Input Voltage | 50 Ω: 5 Vrms; 1 MΩ: 400 Vmax (DC + Peak AC ≤ 5 kHz) |
| Auxiliary Output |
| Connector Type | BNC, located on rear panel |
| Signal Types | Select from control signals or Off |
| Output Signal | 500 Hz-1 MHz square wave or DC level; 50 mV-1 V into 1 MΩ |
| Control Signals | Trigger enabled, trigger out, pass/fail status, off |
| General |
| Auto Calibration | Ensures specified DC and timing accuracy is maintained for 1 year minimum. |
| Power Requirements |
| Voltage | 100-240 VAC ±10% at 45-66 Hz; 110-120 VAC ±10% at 380-420 Hz; Automatic AC Voltage Selection; Installation Category: 300V CAT II |
| Max. Power Consumption | 425 W / 425 VA |
| Environmental and Safety |
| Temperature (Operating) | +5 °C to +40 °C |
| Temperature (Non-Operating) | -20 °C to +60 °C |
| Humidity (Operating) | 5% to 80% relative humidity (non-condensing) up to +31 °C. Upper limit derates to 50% relative humidity (non-condensing) at +40 °C. |
| Humidity (Non-Operating) | 5% to 95% relative humidity (non-condensing) as tested per MIL-PRF-28800F |
| Altitude (Operating) | Up to 10,000 ft. (3048 m) at or below +25 °C |
| Altitude (Non-Operating) | Up to 40,000 ft. (12,192 m) |
| Random Vibration (Operating) | 0.31 grms 5 Hz to 500 Hz, 15 minutes in each of three orthogonal axes |
| Random Vibration (Non-Operating) | 2.4 grms 5 Hz to 500 Hz, 15 minutes in each of three orthogonal axes |
| Functional Shock | 30 g peak, half sine, 11 ms pulse, 3 shocks (positive and negative) in each of three orthogonal axes, 18 shocks total |
| Physical Dimensions |
| Dimensions (HWD) | 11.29"H x 16"W x 8.1"D (287 x 408 x 205 mm) |
| Weight | 22.0 lbs. (9.98 kg) |
| Shipping Weight | 36 lbs. (16.36 kg) |
| Certifications |
| Certifications | CE Compliant, UL and cUL listed; conforms to EN 61326, EN 61010-1, UL 61010-1 2nd edition, and CSA C22.2 No. 61010-1-04 |
| Warranty and Service |
| Warranty and Service | 3-year warranty; calibration recommended annually. Optional service programs include extended warranty, upgrades, and calibration services. |