Specifications

| Features | 190-204 | 190-104 |
| --- | --- | --- |
| Bandwidth | 200 MHz | 100 MHz |
| Max. real time sample rate | 2.5 GS/s | 1.0 GS/s |
| Display | 144 mm Full Color LCD | 144 mm Full Color LCD SCC |
| Digital Persistence | Yes, gives analog oscilloscope like waveform decay (user selectable) | Fluke 19xB: Persistence on/off |
| Envelope mode | Yes |
| Waveform Compare | Visual Reference and Automatic ‘Pass / Fail’ testing | Visual Reference |
| Max. record length in Scope mode: | 1200 points per input channel |
| Max. record length in ScopeRecord mode: | 27,000 points per input or more (5 ms/div…2 min/div.) |
| Number of inputs | 2 plus external / DMM input, all isolated from each other and from ground |
| Number of digitizers | 2 |
| Independently floating isolated inputs | Up to 1000 V between inputs, references and ground |
| Input sensitivity | 2 mV/div. … 100 V/div. | 5 mV/div. … 100 V/div. |
| Glitch capture | Up to 3 ns using Pulse Width triggering; 50 ns peak detect at 5 ms/div. to 1 min/div. |
| Timebase range in Scope mode | 5 ns/div to 2 min/div. | 10 ns/div to 2 min/div. |
| Trigger types | Connect-and-View, Free Run, Single Shot, Edge, Delay, Video Frame, Video line, Selectable pulse width and External |
| Scope Measurements | 7 cursors measurements, 30 automatic measurements |
| Waveform Mathematics | A + B, A – B, A x B, A versus B (X-Y-mode, giving Lissajous diagrams) |
| Scope-Record Trigger modes | Start on Trigger, Stop on Trigger |
| Capture last 100 screens | Automatic, with Replay capability |
| Dual input TrendPlot | Yes, with Cursors and Zoom |
| Memory for screens and set-ups | 10 screens with set-up; 5 more memories are made available upon registration of theScopeMeter |
| Memory for recordings | Two, each can store 100 scope screens, a ScopeRecord or a TrendPlot |
| True RMS multimeter | 5000 counts, Volts, Amps, Ohms, Continuity, Diode, Temp |
| Safety certified (EN61010-1) | 1000 V CAT II / 600 V CAT III (instrument and included accessories) |
| Battery (installed) | 4 hr Ni-MH BP190 |
| Line power | Adapter / battery-charger included |
| Size | 25.6 x 16.9 x 6.4 cm (10.1 x 6.7 x 2.5 inch) |
| Weight | 2 kg |
| PC and Printer interface | Using optional Optically Isolated RS-232 adapter / cable |
| Warranty | 3 years on main instrument, 1 year on the standard accessories |