| Function | Range(3) | Resolution | Input Resistance etc. | 24 Hour 23°C± 1°C | 90 Day 23°C± 5°C | 1 Year 23°C± 5°C | Temperature Coefficient 0°~ 18°C /28°~ 55°C |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DC Voltage | 100.0000 mV | 0.1μV | 10MΩ or >10GΩ | 0.0030 + 0.0030 | 0.0040 + 0.0035 | 0.0050 + 0.0035 | 0.0005 + 0.0005 |
|  | 1.000000 V | 1μV | 10MΩ or >10GΩ | 0.0015 + 0.0004 | 0.0020 + 0.0005 | 0.0035 + 0.0005 | 0.0005 + 0.0001 |
|  | 10.00000 V | 10μV | 11.11MΩ±1% | 0.0020 + 0.0006 | 0.0030 + 0.0007 | 0.0040 + 0.0007 | 0.0005 + 0.0001 |
|  | 100.0000 V | 0.1mV | 10.1MΩ±1% | 0.0020 + 0.0006 | 0.0035 + 0.0006 | 0.0045 + 0.0006 | 0.0005 + 0.0001 |
|  | 1000.000 V | 1mV | 10.1MΩ±1% | 0.0020 + 0.0006 | 0.0035 + 0.0010 | 0.0045 + 0.0010 | 0.0005 + 0.0001 |
| Resistance(4) | 100.0000 Ω | 100μΩ | 1 mA | 0.0030 + 0.0030 | 0.008 + 0.004 | 0.010 + 0.004 | 0.0008 + 0.0005 |
|  | 1.000000 kΩ | 1mΩ | 1 mA | 0.0020 + 0.0005 | 0.008 + 0.001 | 0.010 + 0.001 | 0.0008 + 0.0001 |
|  | 10.00000 kΩ | 10mΩ | 100μA | 0.0020 + 0.0005 | 0.008 + 0.001 | 0.010 + 0.001 | 0.0008 + 0.0001 |
|  | 100.0000 kΩ | 100mΩ | 10μA | 0.0020 + 0.0005 | 0.008 + 0.001 | 0.010 + 0.001 | 0.0008 + 0.0001 |
|  | 1.000000 MΩ | 1μΩ | 3.5μA | 0.0020 + 0.0010 | 0.008 + 0.001 | 0.010 + 0.001 | 0.0010 + 0.0002 |
|  | 10.00000 MΩ | 10Ω | 350nA | 0.0150 + 0.0010 | 0.020 + 0.001 | 0.040 + 0.001 | 0.0030 + 0.0004 |
|  | 100.0000 MΩ | 100Ω | 350 nA//10 MΩ | 0.3000 + 0.0100 | 0.800 + 0.010 | 0.800 + 0.010 | 0.1500 + 0.0002 |
| DC Current | 100.0000 μA | 100pA | < 0.015 V | 0.010 + 0.020 | 0.04 + 0.025 | 0.05 + 0.025 | 0.002 + 0.0030 |
|  | 1.000000 mA | 1nA | < 0.15 V | 0.007 + 0.005 | 0.03 + 0.005 | 0.05 + 0.005 | 0.002 + 0.0005 |
|  | 10.00000 mA | 10nA | < 0.07 V | 0.005 + 0.010 | 0.03 + 0.020 | 0.05 + 0.020 | 0.002 + 0.0020 |
|  | 100.0000 m A | 0.1μA | < 0.7 V | 0.010 + 0.004 | 0.03 + 0.005 | 0.05 + 0.005 | 0.002 + 0.0005 |
|  | 1.000000 A | 1μA | < 0.8 V | 0.050 + 0.006 | 0.08 + 0.010 | 0.10 + 0.010 | 0.005 + 0.0010 |
|  | 10.00000 A | 10μA | < 0.5 V | 0.100 + 0.008 | 0.12 + 0.008 | 0.15 + 0.008 | 0.005 + 0.0008 |
| Continuity | 1000.000 Ω | 0.001Ω | 1 mA | 0.002 + 0.030 | 0.008 + 0.030 | 0.010 + 0.030 | 0.001 + 0.002 |
| Diode Test | 1.000000 V | 1μV | 1 mA | 0.002 + 0.010 | 0.008 + 0.020 | 0.010 + 0.020 | 0.001 + 0.002 |
| True RMS AC Voltage(6) | 100.0000 mV | 0.1μV | 3Hz - 5Hz | 1.00 + 0.03 | 1.00 + 0.04 | 1.00 + 0.04 | 0.100 + 0.004 |
|  |  |  | 5Hz - 10Hz | 0.35 + 0.03 | 0.35 + 0.04 | 0.35 + 0.04 | 0.035 + 0.004 |
|  |  |  | 10Hz - 20kHz | 0.04 + 0.03 | 0.05 + 0.04 | 0.06 + 0.04 | 0.005 + 0.004 |
|  |  |  | 20kHz - 50kHz | 0.10 + 0.05 | 0.11 + 0.05 | 0.12 + 0.05 | 0.011 + 0.005 |
|  |  |  | 50kHz - 100kHz | 0.55 + 0.08 | 0.60 + 0.08 | 0.60 + 0.08 | 0.060 + 0.008 |
|  |  |  | 100kHz -300kHz | 4.00 + 0.50 | 4.00 + 0.50 | 4.00 + 0.50 | 0.200 + 0.020 |
|  | 1.000000 V to 750.000 V(5) | 1μV ~ 1mV | 3Hz - 5Hz | 1.00 + 0.02 | 1.00 + 0.03 | 1.00 + 0.03 | 0.100 + 0.003 |
|  |  |  | 5Hz - 10Hz | 0.35 + 0.02 | 0.35 + 0.03 | 0.35 + 0.03 | 0.035 + 0.003 |
|  |  |  | 10Hz - 20kHz | 0.04 + 0.02 | 0.05 + 0.03 | 0.06 + 0.03 | 0.005 + 0.003 |
|  |  |  | 20kHz - 50kHz | 0.10 + 0.04 | 0.11 + 0.05 | 0.12 + 0.05 | 0.011 + 0.005 |
|  |  |  | 50kHz - 100kHz | 0.55 + 0.08 | 0.60 + 0.08 | 0.60 + 0.08 | 0.060 + 0.008 |
|  |  |  | 100kHz -300kHz | 4.00 + 0.50 | 4.00 + 0.50 | 4.00 + 0.50 | 0.200 + 0.020 |
| True RMS AC Current(6) | 1.000000 mA | 1nA | 3Hz – 5Hz | 1.00 + 0.04 | 1.00 + 0.04 | 1.00 + 0.04 | 0.100 + 0.006 |
|  |  |  | 5Hz – 10Hz | 0.30 + 0.04 | 0.30 + 0.04 | 0.30 + 0.04 | 0.035 + 0.006 |
|  |  |  | 10Hz – 5kHz | 0.10 + 0.04 | 0.10 + 0.04 | 0.10 + 0.04 | 0.015 + 0.006 |
|  |  |  | 5kHz – 10kHz | 0.20 + 0.25 | 0.20 + 0.25 | 0.20 + 0.25 | 0.030 + 0.006 |
|  | 10.00000 mA | 10nA | 3Hz – 5Hz | 1.10 + 0.06 | 1.10 + 0.06 | 1.10 + 0.06 | 0.200 + 0.006 |
|  |  |  | 5Hz – 10Hz | 0.35 + 0.06 | 0.35 + 0.06 | 0.35 + 0.06 | 0.100 + 0.006 |
|  |  |  | 10Hz – 5kHz | 0.15 + 0.06 | 0.15 + 0.06 | 0.15 + 0.06 | 0.015 + 0.006 |
|  |  |  | 5kHz – 10kHz | 0.35 + 0.70 | 0.35 + 0.70 | 0.35 + 0.70 | 0.030 + 0.006 |
|  | 100.0000 mA | 100nA | 3Hz – 5Hz | 1.00 + 0.04 | 1.00 + 0.04 | 1.00 + 0.04 | 0.100 + 0.006 |
|  |  |  | 5Hz – 10Hz | 0.30 + 0.04 | 0.30 + 0.04 | 0.30 + 0.04 | 0.035 + 0.006 |
|  |  |  | 10Hz – 5kHz | 0.10 + 0.04 | 0.10 + 0.04 | 0.10 + 0.04 | 0.015 + 0.006 |
|  |  |  | 5kHz – 10kHz | 0.20 + 0.25 | 0.20 + 0.25 | 0.20 + 0.25 | 0.030 + 0.006 |
|  | 1.000000 A | 1μA | 3Hz – 5Hz | 1.00 + 0.04 | 1.00 + 0.04 | 1.00 + 0.04 | 0.100 + 0.006 |
|  |  |  | 5Hz – 10Hz | 0.30 + 0.04 | 0.30 + 0.04 | 0.30 + 0.04 | 0.035 + 0.006 |
|  |  |  | 10Hz – 5kHz | 0.10 + 0.04 | 0.10 + 0.04 | 0.10 + 0.04 | 0.015 + 0.006 |
|  |  |  | 5kHz – 10kHz | 0.35 + 0.70 | 0.35 + 0.70 | 0.35 + 0.70 | 0.030 + 0.006 |
|  | 10.00000 A | 10μA | 3Hz – 5Hz | 1.10 + 0.06 | 1.10 + 0.06 | 1.10 + 0.06 | 0.100 + 0.006 |
|  |  |  | 5Hz – 10Hz | 0.35 + 0.06 | 0.35 + 0.06 | 0.35 + 0.06 | 0.035 + 0.006 |
|  |  |  | 10Hz – 5kHz | 0.15 + 0.06 | 0.15 + 0.06 | 0.15 + 0.06 | 0.015 + 0.006 |
|  |  |  | 5kHz – 10kHz | 0.35 + 0.70 | 0.35 + 0.70 | 0.35 + 0.70 | 0.030 + 0.006 |
| Frequency / Period | 100.0000mV to 750.000V(5) | ― | 3Hz - 5Hz | 0.1 | 0.1 | 0.1 | 0.005 |
|  |  |  | 5Hz - 10Hz | 0.05 | 0.05 | 0.05 | 0.005 |
|  |  |  | 10Hz - 40Hz | 0.03 | 0.03 | 0.03 | 0.001 |
|  |  |  | 40Hz -300kHz | 0.006 | 0.01 | 0.01 | 0.001 |
| Temperature (RTD) | -200 °C ~ 600 °C | 0.001 °C | ― | ― | ― | 0.06 °C (typical) | 0.005 °C / °C (typical) |
| Temperature (Thermocouple) | -200 °C ~ + 1300 °C | 0.002 °C | E / J / T / K / N | ― | ― | 0.3 °C (typical) | 0.004 °C / °C (typical) |
|  | -50 °C ~ + 1820 °C | 0.01 °C | R / S / B | ― | ― | 1 °C | 0.14 °C / °C |
| Display | VFD, Tow Colors Display | Note : |
| Interface | RS -232C, USB, Digital I/O | 1. All specifications are ensured only under a single display. |
| Power Source | AC 100 V / 120 V / 220 V / 240 V ±10% | 2. Accuracy : ± (% of reading + % of range) |
| Power Line Frequency | 45 Hz to 66 Hz and 360 Hz to 440 Hz | 3. 20% overrange on all ranges, except 1000Vdc, 750Vac and 10A. |
| Power Consumption | Max. 25VA | 4. Resistance is for 4-wire ohms function, or 2-wire ohms with REL on. |
| Dimensions | 265(W) x 107(H) x 350(D) mm | 5. 750Vac range limited to 100kHz |
| Weight | Approx. 3.1kg without option | 6. AC Characteristics are for sinewave input > 5% of range. |